Ideas and information

#sample program
# available commands
# A-out, A-in, B-out, B-in, C-out, C-in, D-out, D-in, E-out, E-in, F-out, F-in, ALU-A-in, ALU-B-in, ALU-out, ALU-sum, ALU-sub, ALU-mul, ALU-div, ALU-and, ALU-or, ALU-equ, ALU-shift, PC-reset, PC-in, PC-out, IR-in, IR-out, SP-in, SP-out, SREG-in, SREG-out, ID-in, ID-out

Multiplexer-type: 74HC253

Multiplexer1:
    A-out, B-out, C-out, D-out, E-out, F-out, ALU-out, PC-out

main:
    ldi regA, regB

#machine-code

03 01 02

#microcode

ldi regA, regB =
    | MR-out, IR-in |
    | A-in, B-out |

#interpretation

Look in memory cell 0x03 for instruction ldi which points to the bits that need to be turned on in the control unit by looking at IR. The bytes is then put on the control bus.

#Ideas

All outputs are connected to a multiplexer the mux gets a control byte for witch to turn on when data comes.
All inputs are connected to a demultiplexer.