Sigma-Computer instruction-set

Instruction Register (IR) size 24-bits (3-bytes)

add – Add operation
ldi – Load into
out – Output

ADD – Add operation

The add operation adds operand 1 and operand 2.

Opcode	description

0x01 16-r1 16-r2	Add two 16-bit registers. R1 contains result
0x02 16-r1 16-num	Add a 16-bit number into 16 bit register r1. R1 contains result
0x02 8-r1 8-num	Add an 8-bit number into 8 bit register r1. R1 contains result

Ex.

00000001 00010010 (0x01 0x16)→ add register B and register A

00000010 00010010 00000000 00000010 (0x02 0x16 0x00 0x02) → add 2 (16-bit) to register A
     ^
      |
iw (specifies word size)

Pseducode:

dst ← dst + src

LDI – Load into

The ldi operation loads operand 2 (src) into operand 1 (dst)

Opcode	description

0x03 r1 r2	Load r2 into r1. Two 16-bit registers

OUT – Output

The out operation outputs regA